## Slide 1: CPE 301
Lab #4 – The LED & GPIO Lab

## Slide 2: Contents:
LEDs
Schematics & Symbols
Arduino Pins, Ports, and Pinouts
Arduino Library

## Slide 3: LEDs
V = I * R
Short Pin / Flat side = Cathode
Anode = ( + )
Cathode = ( - )
Positive potential difference from Anode to Cathode = LIGHT
Overcurrent = POP, then smoke

## Slide 4: Schematics & Symbols
Schematics
  Hand-draw then scan or use CAD:
    Circuitmaker
      steep learning curve, but TONS of features
      very similar to professional software (Altium Designer)
    Circuit-diagram.org
      super easy
      in browser

## Slide 5: Schematics & Symbols
Rules of Thumb
  Labels, Labels, Labels
  Put positive supply on top
  Put ground on bottom

## Slide 6: Schematics & Symbols
Symbols
  LED
  MOSFET
  RESISTOR
  VCC
  Ground
  Button

## Slide 7: Arduino Pins, Ports, and Pinouts
Arduino is a Development Platform
  Easy to use
    simplifies the more complex aspects of programming microcontrollers
  IDE & Libraries
    Simple IDE with integrated USB uploader
    Abstracted libraries
Atmel 2560 is a Microcontroller which Arduino uses in the Mega
  8 bit commercial microcontroller
  Very simple architecture
  Simple Memory Mapped I/O

## Slide 8: Arduino Pins, Ports, and Pinouts
Every I/O Pin:
  Arduino Pin # (1-54, A0-A15)
  Port Name/Number
  Can have many different funcitons
Arduino Pin #s:
  Labeled on the board
  Work with Arduino Library Functions
  Uniform Across all Arduino boards
Atmel 2560 Ports
  Specific to the microcontroller
  Allow direct access to hardware = ultimate control

## Slide 9: Arduino Library
Basic Functions:
# | Name | Description | Parameters
1 | pinMode | Sets up pin for input or output | Pin # INPUT/OUTPUT/INPUT_PULLUP
2 | digitalWrite | Sets state of output pin | Pin # HIGH/LOW
3 | digitalRead | Reads state of input pin | Pin #
4 | delay | Waits a number of milliseconds | # of milliseconds

## Slide 10: Arduino Library
RULES FOR THE REST OF THE SEMESTER
After this lab -> NO ARDUINO LIBRARY (unless specifically stated)
  Homework
  Labs
  Quizzes
  Tests
  Still ok to use for debugging…